### Comments on list

This list takes the substances as its starting point and discusses hazardous waste and waste which requires particular attention or is difficult to classify. Electrical waste is discussed in a specific section at the end. The list is intended to be an aid, but the waste producer must take responsibility for how the waste is to be classified.

For materials and products in alphabetical order, see Appendix 5, Search list – materials and products from demolition/exchange.

For handling waste which is not hazardous waste, see Appendix 4, Waste fractions – overall list.

The list provides a number of examples but does not cover all types of hazardous waste which may occur. See also Chapter 6 in the Resource and Waste Guidelines.

### Explanations

HW = Hazardous waste

An asterisk (*) after the waste code means that the waste is hazardous (the same designation as in the Swedish Waste Ordinance).

The Handling, legal requirements column: The column describes only special legal requirements to note. In general you are referred to the requirements of the Environmental Code, the Waste Ordinance and the Ordinance on Environmentally Hazardous Operations and Health Protection and other legal requirements which are described in Appendix 18, Waste rules.

The Handling, industry standards column: The column is the construction sector's interpretation of legal requirements or exceeds legal requirements.

“Incineration in an approved facility” means incineration in a facility that fulfils the rules for waste incineration and has authorisation to incinerate the relevant waste.

“Approved recipient” and “Approved pretreatment facility” refer to recipients and pretreatment facilities which have authorisation to receive the relevant waste type.

### Hazardous waste, including electrical waste

According to the legislation, hazardous waste should be sorted from other waste. Different types of hazardous waste may not be mixed with each other. Nor may hazardous waste be mixed with other types of waste or with other substances or materials (Section 16 of the Swedish Waste Ordinance). The owner of waste which contains or consists of electrical and electronic products shall sort the electrical and electronic products and submit these to a collection system or ensure that they are treated in an acceptable manner from a health and environmental viewpoint (Section 25 of the Swedish Waste Ordinance).

### The list's waste codes

For many types of waste it is difficult to assess and know how they should be disposed of. The waste codes stated in the list are suggested codes. The code which should be stated depends on the origin and characteristics of the waste. The list contains a number of question marks for waste types where handling is uncertain or the waste has two different codes, where one states that it is hazardous waste. Where there is any doubt, a more detailed investigation of what the waste contains and an assessment of how it should be classified is then carried out in each individual case. The Swedish Waste Ordinance contains provisions stating that waste shall be considered as hazardous waste if the concentrations of substances with certain hazardous characteristics exceed certain levels. Use the precautionary principle. This means that if it is not possible or reasonable to sufficiently investigate the characteristics of the waste, but there is reason to suspect that it can be hazardous, the waste shall be handled as hazardous waste.

Guidance for the classification of hazardous waste is available on the Swedish Environmental Protection Agency's website and in the Swedish Waste Management's reports from 2004 about the classification of hazardous waste. See also Appendix 18, Waste rules.

### Project adaptation

The list is intended to be adapted to the current project by means of deletions and additions in order to describe the handling of the hazardous waste involved in the project.

| The project Discovered during inventory | Substance | Example of occurrence (material/product) | Waste code | From demolition/exchange | From production | Handling, legal requirements | Handling, industry standards | Miscellaneous |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Aerosols | Spray cans | 08 01 11* if paint 08 05 01* if isocyanates (e.g. jointing foam) | X (remaining) | X | Hazardous goods |  | Flammable. Can be recycled or incinerated |
|  | Arsenic | Pressure impregnated timber | 17 02 04* | X | X | Requires no specific protection/actions during handling/sorting | All pressure impregnated timber is handled as HW. Sorted into specific containers for transport to approved incineration facility. |  |
|  | Asbestos (general information on asbestos) |  | See relevant product |  |  | Asbestos is defined in AFS 2006:1. Note occupational health and safety requirements! For legal requirements during handling, see AFS 2006:1. If there is a risk for release of fibres, the decontamination area shall have airlocks and underpressure ventilation. Asbestos material shall be packaged in closed and sealed containers which shall be marked. | Hard sheet material and similar shall be dismantled and packaged whole if possible. Glues and paints should be sanded and the dust picked up with a vacuum cleaner. The basic rule for looser asbestos products is that they should be sanded/dismantled and sucked into a closed container. Alternatively, the material should be demolished and packed in sacks. | Landfill Occupational health and safety requirements include requirements in terms of training and preventing the spread of fibres. |
|  | Asbestos | Acoustic tiles, hard | 17 06 01* | X |  |  | Handled whole |  |
|  | Asbestos | Fire doors (insulation) | 17 06 01* | X |  |  | Decontamination or scrapping of entire door. |  |
|  | Asbestos | Eternit tiles or sheets | 17 06 05* | X |  |  | Handled whole |  |
|  | Asbestos | Paint and filler | 17 06 05* | X |  |  | Sanding |  |
|  | Asbestos | Windowsills | 17 06 05* | X |  |  | Handled whole |  |
|  | Asbestos | Spark protection in electrical installations | 16 02 13* | X |  | Electrical waste, should go to pretreatment | The entire electrical product is treated as electrical waste and sent to an approved pretreatment facility. |  |
|  | Asbestos | Floor coverings in PVC | 17 06 05* | X |  |  | Demolition and sanding |  |
|  | Asbestos | Insulation with sprayed asbestos (e.g. around steel constructions) | 17 06 01* | X |  |  | Scrapping of entire product or demolition |  |
|  | Asbestos | Insulation material e.g. around cooling and heating pipes | 17 06 01* | X |  |  | Scrapping of entire product or demolition |  |
|  | Asbestos | Tile adhesive and grout | 17 06 05* | X |  |  | Demolition |  |
|  | Asbestos | Condensation insulation | 17 06 01* | X |  |  | Scrapping of entire product or demolition |  |
|  | Asbestos | Magnesite used as a screed material in WCs, cloakrooms or other smaller spaces | 17 06 05* | X |  |  | Mechanical demolition | Occurred primarily during the period 1910-1930. |
|  | Asbestos | Gaskets in boilers and pipe systems | 17 06 01* | X |  |  | Removal of gaskets |  |
|  | Asbestos | Tar adhesive, e.g. in floors | 17 06 05* | X |  |  | Sanding and/or milling. Decontaminated by company with specific expertise. | Occurred before the ban 1976. |
|  | Asbestos | Sealants around sheet metal ventilation ducts | 17 06 05* | X |  |  | Scrapping of entire products or cutting out asbestos e.g. by taping over the sealant and cutting or disc grinding away the part of the sheet metal (including a margin) which is contaminated with asbestos. |  |
|  | Asbestos | Ventilation ducts in Eternit or other products containing asbestos | 17 06 05* | X |  |  | Scrapping of entire product |  |
|  | Alkaline waste | Chemicals e.g. cleaning products, caustic soda | 20 01 15* | X | X |  |  |  |
|  | Pesticides | Timber attacked by pests can contain pesticides | 17 02 04* | X |  | Shall be decontaminated/removed before demolition | It is important that insects are not spread during demolition and waste handling. Trying to organise transport that ensures that pests are not spread. | NB This can be an occupational health and safety problem Incineration in approved facility |
|  | Lead, metallic | Lead, in electrical cables | 17 04 11 | X |  | Electrical waste, should go to pretreatment | Lead cables are sorted on site and sent to an approved pretreatment facility | Material recovery |
|  | Lead, metallic | Leaded glass | 17 04 03 | X |  |  | The lead is collected together on site in order to be sent to an approved recipient | Material recovery |
|  | Lead, metallic | Lead alloyed brass and bronze | 17 04 01 | X |  |  | Disposed of separately and sent to an approved recipient | Material recovery |
|  | Lead, metallic | Sheet lead radiation protection | 17 04 03 | X | X |  | The lead is collected together on site in order to be sent to an approved recipient | Material recovery |
|  | Lead, metallic | Cable shielding and sheathing of lead | 17 04 11 | X |  |  | Should be sorted separately to facilitate material recovery of lead. Do not mix with other cables. Should be sent directly to approved recipient. | Material recovery |
|  | Lead, metallic | Joints in waste pipes (lead packing) | 17 04 03 | X |  |  | Sent together with the pipes to approved recipient. | Material recovery |
|  | Lead contaminants | Lead batteries | 16 06 01* | X | X | Ordinance on producer responsibility for batteries, 2008:834 | Sent for transport by authorised contractor. | Material recovery |
|  | Lead contaminants | Joint compounds | 17 09 03* | X |  |  | HW |  |
|  | Lead contaminants | Paint layer (dried) which can contain lead (white lead, red lead etc.) | 17 02 01 (wood) 17 04 05 (iron and steel) 12 01 16* (sandblasted paint layer) | X |  | Residues from sanding and blasting of paint containing lead are collected and handled as HW. | Wood painted with paints containing lead can be classified as hazardous waste and therefore should be assessed individually. Steel with paints containing lead is handled as metal. | Sandblasting waste is disposed of to landfill. Wood is incinerated in a facility that has authorisation to incinerate painted wood. |
|  | Lead contaminants | Tiles, roof tiles with lead glaze | 17 01 03 | X |  |  |  | Should be possible to use as aggregates at a controlled landfill site (?) |
|  | Lead contaminants | PVC pipes (e.g. waste pipes) and other PPC products with lead stabilisers | 17 02 03 | X |  |  | See PVC |  |
|  | Lead contaminants | PVC matting | 17 02 03 | X |  |  | See PVC |  |
|  | Brominated flame retardants | Cellular rubber insulation (black cooling insulation), of Armaflex type. There are also other condensation insulation materials with brominated flame retardants. | 17 06 03*? 17 06 04? | X |  | The POP ordinance, Ordinance (EU) no. 850/2004 | Two types of Armaflex exist with different contents of flame retardant: Armaflex insulation which is marked NH (no halogen) does not contain bromine and is not classified as hazardous waste. Armaflex marked with AF or unmarked insulation contains bromine and is classified as hazardous waste. If dismantling is easy, separate installation, otherwise treat everything as HW. In the case of uncertainty, sampling is recommended. | Incineration in approved facility. |
|  | Brominated flame retardants | Cellular plastic insulation (e.g. soft white insulation around soft copper pipes) | 17 06 03*? 17 06 04? | X | X? | The POP ordinance, Ordinance (EU) no. 850/2004 | Handled as HW. | Incineration in approved facility. |
|  | Brominated flame retardants | PP or PE plastic e.g. in edging strips, plastic parts of fans etc. | 17 02 03*? 17 02 04? | X | X? | The POP ordinance, Ordinance (EU) no. 850/2004 | Handled as HW. | Incineration in approved facility. |
|  | Brominated flame retardants | Textiles | 17 09 03* or 17 09 04 | X |  | The POP ordinance, Ordinance (EU) no. 850/2004 | Look for information in the goods declaration and care instructions in order to be able to release the item. Otherwise handled as HW. In which case sorted into specific container. |  |
|  | CFCs, HCFCs, HFCs | Refrigeration and freezing units CFCs, HCFCs as cooling media | 16 02 11* (if scrapped equipment containing HCFCs or CFCs) 14 06 01* (if HCFCs or CFCs) | X |  | Electrical waste. | Sorted separately. Handled as separate package and sent to approved pre-treatment facility. | Producer responsibility for refrigerators and freezers. |
|  | CFCs, HCFCs, HFCs | Cooling facilities, air-conditioning units As cooling media | 16 02 11* (if scrapped equipment containing HCFCs or CFCs) 14 06 01* (if HCFCs or CFCs) | X |  | The cooling medium is HW. The cooling system is emptied of cooling media and ester oils by a cooling services company with certified staff. The ordinance (2016:1128) on fluorinated greenhouse gases and the EU’s f-gas regulation (517/2014) Emptied cooling facilities are electrical waste. | Current facilities are emptied of cooling medium on site and then sent to an approved pretreatment facility. Smaller air handling units which can be handled whole can be deposited at an approved pretreatment facility. | Destruction |
|  | CFCs | Cellular plastic insulation. Found, for example as flooring sheets, insulation in walls and floating floors, refrigerators and freezers, cold rooms. | 17 06 03* | X |  |  | If uncertain regarding CFC content: take sample for analysis or handle as CFCs. The basic rule is to submit material for destruction of CFCs instead of landfill. Landfill should be avoided! CFCs leak out into the environment in the case of landfill. |  |
|  | Halons | Fire extinguisher equipment containing halons | 16 05 04* | X |  |  | Sent for destruction |  |
|  | Dry rot | Timber attacked by dry rot | 17 02 04* | X |  |  | Ensure that dry rot is not spread when the timber is demolished and handle demolished materials so that dry rot spores are not spread. Do not send for material recovery. Sent for incineration in approved facility. Inform the receiving waste contractor. | Local regulations, different in different municipalities. Specialist knowledge is required to carry out an inventory of dry rot. |
|  | Cadmium | Waste pipes of plastic with cadmium | 17 02 04*? | X |  |  | If cadmium content is suspected or observed through laboratory analysis: handled as HW. |  |
|  | Cadmium | Electrical cables in yellow, orange and red shades | 17 04 10*? | X |  |  | Electrical waste. Sorted separately and sent to an approved pretreatment facility. |  |
|  | Cadmium | Floor coverings of PVC in light shades of yellow, orange and red | 17 02 04*? | X |  |  | If cadmium content is suspected or observed through laboratory analysis: handled as HW. | May apply to floor coverings laid before 1982, when cadmium was prohibited in Sweden as a plastic additive. |
|  | Cadmium | Tiles (and other glazed ceramic material) in light shades of yellow, orange and red. | 17 01 03? 17 01 06*? | X |  | Environmental Impact Assessment ordinance (2013:251), Chapter 29, sections 34 and 35 | If cadmium content is suspected or observed through laboratory analysis: dismantle and handle carefully so that the material is not crushed. Handled separately. The waste owner must investigate whether, for example, recycling for construction purposes is an alternative. Notifications or applications for permits are required if the contamination risk is low or more than low. |  |
|  | Cadmium | Nickel-cadmium batteries | 16 06 02* | X | X | The ordinance on producer responsibility for batteries (SFS 2008:834) | Remove any batteries in emergency lighting luminaires or which provide backups for alarm systems before demolition. Car batteries and open nickel-cadmium batteries shall be stored in acid resistant containers and transported by approved transporters to approved recipients. |  |
|  | Chemicals, various | Chemical residues: joint compound, paint, varnish, adhesive, solvents etc. | 08 01 11* for paint and solvents. Waste code can vary depending on origin. | X (remaining) | X | If the packaging is marked with the skull hazard symbol (very toxic, T+, toxic, T) or dead fish (environmentally hazardous, N), it shall be handled as hazardous waste. Older, unmarked chemical products which cannot be identified should also be handled as hazardous waste. | The basic rule is that all chemical residues should be handled as HW. Only clean items of packaging can be sent for material recovery. |  |
|  | Chlorinated paraffins | Joint compounds and in sealing compound in insulated window panes | 17 09 03* | X |  | The POP ordinance, Ordinance (EU) no. 850/2004 | If joint compounds with chlorinated paraffins contain more than 2500 mg/kg (0.25%) SCCP/MCCP), they must be treated as hazardous waste. If the levels of short-chain chlorinated paraffins (SCCPs) are in excess of 10,000 mg/kg (1%), the waste must also be handled according to the POP ordinance’s requirements for destruction or irreversible transformation. In practice this can mean combustion of the waste in facilities with permits for this. |  |
|  | Chlorinated paraffins | PVC floor coverings, safety flooring | 17 09 03* | X |  | The POP ordinance, Ordinance (EU) no. 850/2004 |  | Combustion in hazardous waste combustion facilities |
|  | Copper contaminants | Impregnated timber | 17 02 04* | X | X |  | See “arsenic”, pressure impregnated timber | Incineration in approved facility |
|  | Copper, metallic | Copper cable | 17 04 11 | X | X | Electrical waste | Cable without hazardous substances should be sorted separately and sent to an approved cable granulator or to a recipient which is permitted to handle electrical waste. | Metal recycling |
|  | Copper, metallic | Copper pipes | 17 04 01 | X | X |  | Sorted as metal | Metal recycling |
|  | Creosote | Impregnated timber/sleepers | 17 02 04* | X |  |  | All pressure impregnated timber is handled as HW. Sorted into specific containers for transport to approved incineration facility | Incineration in approved facility |
|  | Chromium, metallic | Surface treatment of metal | 17 04 05 | X | X |  | Sorted as metal | Metal recycling |
|  | Chromium contaminants | Impregnated timber | 17 02 04* | X | X |  | See “arsenic”, pressure impregnated timber | Incineration in approved facility |
|  | Mercury | Deposits in waste pipes and water traps. | 17 09 01* | X |  | Decontamination following remediation measures, requires notification. | Decontamination shall be carried out by an authorised company: The extent, type of pipe and condition determine the choice of decontamination method. High-pressure washing of pipes with collection and cleaning of the flush water may be appropriate. |  |
|  | Mercury | Batteries | 16 06 03* Batteries | X |  | Ordinance on producer responsibility for batteries, 2008:834 | Sorted separately |  |
|  | Mercury | Components in fixed installations which are not covered by producer responsibility. | 16 02 13* 16 02 15* hazardous components removed from scrapped equipment | X |  | Electrical waste | If possible sort the components containing mercury and be extra careful with these. Components containing mercury which are at risk of breakage should be dismantled and disposed of separately. Sent to approved pretreatment facility. Cf electrical waste below. | See the Swedish Environmental Protection Agency’s report 5279, Finding mercury in technical goods and products. |
|  | Mercury | Fluorescent tubes, compact fluorescent tubes | 20 01 21* | X |  | Electrical waste | Sorted separately and sent to an approved pretreatment facility. | Producer responsibility |
|  | Mercury | Electrical installations and instruments | 16 02 13* | X |  | Electrical waste | Sorted separately and sent to an approved pretreatment facility. | Producer responsibility |
|  | Mercury | Sludge and flush water containing mercury | 20 01 21* | X |  |  | Shall be handled by an authorised decontamination company. Cf mercury in waste pipes above. |  |
|  | Mould | Timber attacked by mould | 17 02 01? | X |  |  | Handled so that spread of mould is prevented. | NB This can be an occupational health and safety problem |
|  | Oil, coal tar etc. | Cables | 17 04 10* | X |  | Electrical waste | Sorted separately, i.e. separately from other cables, and sent to approved pretreatment facility. |  |
|  | Oil | Oil filters | 16 01 07* | X | X? |  |  |  |
|  | Oil | Oil-containing drilling sludge and other drilling waste | 01 05 06* | X | X? |  |  |  |
|  | Oil | Rags, Absol etc. contaminated with oil | 15 02 02* | X | X |  |  |  |
|  | Oil | Concrete and other soils contaminated with oil | 17 01 06* or 17 01 07 | X |  | HW depends on oil content. Environmental Impact Assessment ordinance (2013:251), Chapter 29, sections 34 and 35 | If contamination with oil is suspected, this should be investigated and if necessary samples taken for laboratory analysis. The waste owner must investigate whether, for example, recycling for construction purposes is an alternative. Notifications or applications for permits are required if the contamination risk is low or more than low. |  |
|  | Oil | Hydraulic fluid | 13 01 13* | X | X? | Waste oil should, to the extent it is technically feasible and economically reasonable, not be mixed with other types of waste oils or other types of waste in such a way that impedes processing (Swedish Waste Ordinance) |  |  |
|  | PAHs | Asphalt | 17 03 01* or 17 03 02 | X |  | Depends on content of hazardous substances See also AFS 2000:4, “Chemical work environment risks” | PAH = polyaromatic hydrocarbons Tar asphalt with PAHs: In the case of levels of PAH16 > 1000 mg/kg DS, is handled as hazardous waste. Contact the municipality for consultation regarding use of asphalt with PAH levels of 70-1000 mg/kg (can be considered subject to notification). Also contact the municipality for consultation regarding the use of asphalt with PAH levels of less than 70 mg/kg. This can be regarded as unsuitable for use, for example as aggregates. | Asphalt manufactured before 1975 can contain PAHs. The Swedish Transport Administration's guidelines, see the Swedish National Road Administration’s publication 2004:90, Handling of coatings containing tar. Stockholm and Gothenburg have joint guidelines: See SBUF project 11 359, www.sbuf.se The guidelines only apply to use in road constructions. According to the Swedish Environmental Protection Agency's general guidance, waste containing PAH 16 with levels > 300 ppm should be classified as hazardous waste. |
|  | PAHs | Insulation fill | 17 03 03* or 17 09 03* if HW otherwise 17 09 04? | X |  |  | According to the Swedish Environmental Protection Agency's general guidance, waste containing PAH 16 with levels > 300 ppm should be classified as hazardous waste. Benzo[a]pyrene with levels over 50 mg/kg is HW. | Reference. See above. In order to release materials, the levels for both contaminants must be lower than those stated. |
|  | PAHs | Tar paper | 17 09 03* Concrete is classified as 17 01 06* | X |  |  | Weatherproofing layers on concrete should be milled away, becoming HW. | According to the Swedish Environmental Protection Agency's general guidance, waste containing PAH 16 with levels > 300 ppm should be classified as hazardous waste. |
|  | PCBs | Acrydur type floor coatings Joint compounds | 17 09 02* | X |  | See ordinance (2007:19) on PCBs etc. Decontaminated and handled separately. Materials with 50 mg of PCBs per kilo or more are HW. Hazardous goods if > 50 mg/kg. NB occupational health and safety requirement in the case of decontamination, several AFSs. The POP ordinance, Ordinance (EU) no. 850/2004 | Decontaminated by company with specific expertise. PCB-containing materials from a building shall be collected carefully and both ground cover and tight sealing against the building are required. For levels immediately below 50 mg/kg, contact the local environmental authority regarding appropriate handling. Joint and floor compounds with levels of PCBs in excess of 500 mg/kg (0.05% by weight) both internally and externally shall be decontaminated. (Should be finished on 30 June 2016.) During decontamination indoors, protective measures shall be taken in essentially the same way as for asbestos decontamination. | See also Section 6.3, Handling of certain types of waste from demolition in the Resource and Waste Guidelines, together with www.sanerapcb.nu See also Rex G et al. Spreading of PCBs from joint compounds (Spridning av PCB från fogmassor). (Chapter 7, Literature and websites in the Resource and Waste Guidelines) |
|  | PCBs | Insulated window panes, as for sealing compound | 17 09 02* | X |  | See ordinance (2007:19) on PCBs etc. Hazardous goods if > 50 mg/kg. NB occupational health and safety requirement The POP ordinance, Ordinance (EU) no. 850/2004 | Dismantled and handled whole. | Reference. See PCBs above. See also Dismantling and handling of insulated window panes with PCBs (Chapter 7, Literature and websites in the Resource and Waste Guidelines) |
|  | PCBs | Cables with oils containing PCBs (more than 2 wppm PCB) | 17 04 10* | X |  | See ordinance (2007:19) on PCBs etc. Sorted and handled separately from other cables. The POP ordinance, Ordinance (EU) no. 850/2004 |  |  |
|  | PCBs | Condensers | 17 09 02* Separate condensors: 16 02 09* | X |  | See ordinance (2007:19) on PCBs etc. Electrical waste. Hazardous goods if > 50 mg/kg. If leaking condensers: also occupational health and safety requirement! The POP ordinance, Ordinance (EU) no. 850/2004 | Regardless of condensor type, fluorescent luminaires shall be sent to approved recipients of electrical waste for pretreatment including condensor. Condensors shall not be dismantled! | Reference. See PCBs above. |
|  | PCBs | Concrete etc. with PCBs as contaminants | 17 01 01 (concrete), 17 01 02 (brick) or 17 09 02* | X |  | See ordinance (2007:19) on PCBs etc. If the contaminated concrete is HW or not depends on the level of PCBs. Materials with 50 mg of PCBs per kilo or more are HW. Hazardous goods if > 50 mg/kg. The POP ordinance, Ordinance (EU) no. 850/2004 | If contamination is suspected, this should be investigated and if necessary samples taken for laboratory analysis. Sampling should take place during material inventory. Decontaminated by company with specific expertise. During decontamination indoors, protective measures shall be taken in essentially the same way as for asbestos decontamination. Concrete or brick adjacent (or adjacent prior to previous decontamination) to joint compound with approx. 10% PCB: Remove 3 cm or more of the edge before recycling the other material. You should ideally take samples of the edges for assessment. The waste from the edge is handled as HW if the levels are in excess of 50 mg/kg. The waste owner must investigate whether, for example, recycling for construction purposes is an alternative. Notifications or applications for permits are required if the contamination risk is low or more than low | Reference. See PCBs above. |
|  | Pentachlorophenol (PCP) | Wood | 17 02 04* | X |  | The POP ordinance, Ordinance (EU) no. 850/2004 | Be careful when wood is being inserted into buildings, to ensure that pentachlorophenol-treated timber is not classified as clean by mistake! Wood suspected of containing or observed to contain pentachlorophenol is HW and should be sent for incineration in an approved facility. | See Appendix 5, Search list, “Impregnated timber” for years. |
|  | PVC | Plastic matting, watertight membranes, pipes, edging strips etc. | 17 02 03 can be 17 02 04*? | X | X |  | Investigate the opportunities for recycling of PVC pipes via NPG, vinyl flooring via Tarkett, installation waste via the Swedish Flooring Trade Association’s GBR Floor recycling system and PVC coated fabric via the manufacturers. Some suppliers will also take back end-of-life floors. Otherwise the waste can be sent for incineration in an approved facility. Landfill as a final option, if exemption is granted. | PVC containing cadmium. See cadmium. See also Section 6.4.15, Handling of certain types of waste from demolition in the Resource and Waste Guidelines. |
|  | Radioactive substances | Fire detectors | 16 02 13* | X |  | Electrical waste. The Swedish Radiation Safety Authority's regulations on fire detectors which contain radioactive sources with radioactive substances, SSMFS 2008:47. | Fire detectors shall be handled whole and not damaged. Sent to an approved pretreatment facility for electrical waste. Contact El-Kretsen for information about collection. |  |
|  | Radioactive substances | Smoke detectors etc. | - | X |  | Other legislation applies to radioactive waste, the waste does not have a waste code. Scrapped detectors are radioactive waste and should therefore be disposed of according to Section 13 of the Swedish Radiation Protection Act (SFS 1988:220). | See marking for whether it is a smoke or heat detector. Should not be sent to the municipality’s recycling centre. Returned to the producer. Contact the Swedish Radiation Safety Authority for current information. |  |
|  | Radon | Blue concrete | 17 01 07 | X |  | Environmental Impact Assessment ordinance (2013:251), Chapter 29, sections 34 and 35 | Crushing. The waste owner must investigate whether, for example, recycling for construction purposes is an alternative. Notifications or applications for permits are required if the contamination risk is low or more than low. | Can potentially be recycled as construction soils for landfill. |
|  | Pests | Timber attacked by pests | 17 02 01 | X |  | The planning and construction ordinance sets requirements for the extermination of wood-destroying insects in a building to be demolished. | Timber attacked by pests which does not contain pesticides does not need to be classified as hazardous waste, but should still be removed before other demolition is begun. Ensure that pests are not spread during demolition of the timber. Organise transport that guarantees pests are not spread. | Incineration in approved facility. |
|  | Tar | Roofing felt | 17 03 02 17 03 03* | X |  |  | Tar paper containing coal tar is classified as hazardous waste |  |
|  | Tar | Waterproofing layers in wet rooms | 17 03 02 17 03 03*? | X |  |  | If containing coal tar: classified as hazardous waste |  |
|  | Can contain, for example, asbestos, lead, CFCs, HCFCs, mercury, oil, coal tar | Electrical waste, general |  | X | X | In general: SFS 2014:1075 on producer responsibility for electrical equipment, ordinance (2000:208) on producer responsibility for light bulbs and certain luminaires and NFS 2005:10 on professional treatment of waste constituted by electrical or electronic products. | All electrical waste is regarded as HW until demonstrated otherwise. Sorted into separate factions as below or according to the waste contractor and sent to approved recipient of hazardous waste or approved pretreatment facility for electrical waste. Handle waste carefully and avoid damage which can mean that hazardous substances leak out and further impede processing of the waste. |  |
|  |  | Electrical waste: Products covered by producer responsibility: Luminaires, electrical hand tools, IT equipment, office appliances, refrigeration and freezing units and other white goods, telecommunications equipment etc. | 20 01 21* if mercury, 20 01 23* if (CFC) chlorofluorocarbons, 20 01 35* if other hazardous components | X | X | Products covered by producer responsibility: telecoms/IT m.m. There are some interpretation difficulties. The owner of electrical waste shall send it to a collection system which a municipality, producer or other body provides for the purpose (Swedish Waste Ordinance). The products covered by producer responsibility should be disposed of according to the producer’s instructions. See also | Hantera vitvaror som lösa kollin, annat placeras i burar (t.ex. småapparater) eller mindre kärl. Ljuskällor demonteras ur armaturer, i övrigt demonteras inga komponenter. Ljuskällor sorteras lämpligen som lysrör, kompaktlysrör, kvicksilver- och natriumlampor samt glödlampor. Neonrör bör sitta kvar i armaturen. Beträffande hantering av CFC se CFC i listan ovan. | Av bilaga 1 i förordning (2014:1075) om producentansvar för elutrustning framgår det för vilka produkter producentansvar gäller. Beträffande producentansvar, se även www.elkretsen.se. |
|  |  | El-avfall: Fasta installationer och maskiner som inte omfattas av producentansvar: T.ex. tryckvakter, flödesmätare, reläer och kontaktorer, manometrar, el- och elektronikcentraler, motorer, apparater innehållande CFC m.m. | 16 02 09* – 16 02 13* | X |  |  | Hanteras varsamt, det yttre höljet får ej skadas. Sortera om möjligt ut de produkter som innehåller kvicksilver och var extra försiktig med dessa. Komponenter med kvicksilver som riskerar att gå sönder demonteras och tas omhand separat. Beträffande hantering av CFC se CFC i listan ovan. |  |
|  |  | El-avfall: Kablar som innehåller olja, stenkolstjära eller andra farliga ämnen: Kabel i mark, metallomspunnen kabel som servis in i hus | 17 04 10* | X |  |  | Farligt avfall. Sorteras skilt från andra kablar. |  |
|  |  | El-avfall: Kabel i övrigt: Vanlig installations- och anslutningskabel | 17 04 11 | X | X | El-avfall | Kabel utan farliga ämnen sorteras separat och skickas till godkänd kabelgranulerare eller till en mottagare som får hantera el-avfall. |  |